## Slide 1
Chapter 6: Architecture
Machine Language

## Slide 2
Machine Language
Binary representation of instructions
Computers only understand 1’s and 0’s
32-bit instructions
  Simplicity favors regularity: 32-bit data & instructions
4 Types of Instruction Formats:
  R-Type
  I-Type
  S/B-Type
  U/J-Type

## Slide 3
R-Type
Register-type
3 register operands:
  rs1, rs2: source registers
  rd: destination register
Other fields:
  op: the operation code or opcode
  funct7,funct3:
  the function (7 bits and 3-bits, respectively)
  with opcode, tells computer what operation to perform

## Slide 4
R-Type Examples

## Slide 5
Chapter 6: Architecture
Machine Language:
More Formats

## Slide 6
I-Type
Immediate-type
3 operands:
  rs1: register source operand
  rd: register destination operand
  imm: 12-bit two’s complement immediate
Other fields:
  op: the opcode
    Simplicity favors regularity: all instructions have opcode
  funct3: the function (3-bit function code)
    with opcode, tells computer what operation to perform

## Slide 7
I-Type Examples

## Slide 8
S/B-Type
Store-Type
Branch-Type
Differ only in immediate encoding

## Slide 9
S-Type
Store-Type
3 operands:
  rs1: base register
  rs2: value to be stored to memory
  imm: 12-bit two’s complement immediate
Other fields:
  op: the opcode
    Simplicity favors regularity: all instructions have opcode
  funct3: the function (3-bit function code)
    with opcode, tells computer what operation to perform

## Slide 10
S-Type Examples

## Slide 11
B-Type
Branch-Type (similar format to S-Type)
3 operands:
  rs1: register source 1
  rs2: register source 2
  imm12:1: 12-bit two’s complement immediate – address offset
Other fields:
  op: the opcode
    Simplicity favors regularity: all instructions have opcode
  funct3: the function (3-bit function code)
    with opcode, tells computer what operation to perform

## Slide 12
B-Type Example
The 13-bit immediate encodes where to branch (relative to the branch instruction)
Immediate encoding is strange
Example:

## Slide 13
U/J-Type
Upper-Immediate-Type
Jump-Type
Differ only in immediate encoding

## Slide 14
U-Type
Upper-immediate-Type
Used for load upper immediate (lui)
2 operands:
  rd: destination register
  imm31:12:upper 20 bits of a 32-bit immediate
Other fields:
  op: the operation code or opcode – tells computer what
  operation to perform

## Slide 15
U-Type Example
Upper-immediate-Type
Used for load upper immediate (lui)
2 operands:
  rd: destination register
  imm31:12:upper 20 bits of a 32-bit immediate
Other fields:
  op: the operation code or opcode – tells computer what
  operation to perform

## Slide 16
J-Type
Jump-Type
Used for jump-and-link instruction (jal)
2 operands:
  rd: destination register
  imm20,10:1,11,19:12: 20 bits (20:1) of a 21-bit immediate
Other fields:
  op: the operation code or opcode – tells computer what
  operation to perform
Note: jalr is I-type, not j-type, to specify rs1

## Slide 17
J-Type Example
0xABC04 – 0x540C =
0XA67F8

## Slide 18
Review: Instruction Formats

## Slide 19
Design Principle 4
Good design demands good compromises
Multiple instruction formats allow flexibility
  add, sub: use 3 register operands
  lw, sw, addi: use 2 register operands and a constant
Number of instruction formats kept small
  to adhere to design principles 1 and 3 (simplicity favors regularity and smaller is faster).